H
R
F
HDL, RTL and FPGA: Lab 1
Your first step in designing digital hardware
Yuri Panchul, Senior Hardware Design Engineer, MIPS
Lecture for Innopolis University - 2018-01-25

---
The informal explanation of acronyms
The informal explanation of acronyms
HDL - Hardware Description Language
  - A language to design, simulate and verify circuits. We will use Verilog-2001.
- RTL - Register Transfer Level
  - A methodology to describe a circuit using HDL in a way that allows semi-automated conversion of the code into a blueprint for a physical chip manufactured on a foundry
- ASIC - Application-Specific Integrated Circuit
  - An example of ASIC is a chip that runs Android on your smartphone
- SoC - System on Chip
  - An ASIC that has one or several processor cores, memories and other components that form the whole computer system on a single chip
- FPGA - Field-Programmable Gate Array
  - A reconfigurable chip we will use as a substitute for manufacturing an ASIC

---
Hardware/software dualism - an informal example
Hardware/software dualism - an informal example
Microcontroller (embedded chip, ASIC, SoC)
CPU
Designed
in Verilog
Executes
instructions
Memory
Contains a program,
a sequence of instructions
Compiled from C
or a similar language
18800005
00001025
00451021
0044182a
5460fffe
00451021
03e00008
00000000

---
Hardware/software dualism - an informal example / 2
Hardware/software dualism - an informal example / 2
Microcontroller (embedded chip, ASIC, SoC)
CPU
Memory
FLASH
Memory
RAM
I/O device controllers
(designed using Verilog too)
18800005
00001025
00451021
0044182a

---
Software: from C to processor instructions
Software: from C to processor instructions
C:
int f (int a, int b)
{
    int s = 0;
    while (s < a)
        s += b;
    return s;
}
Assembly:
sum:
        blez $4, exit
        move $2, $0
        addu $2, $2, $5
loop:
        slt $3, $2, $4
        bnel $3, $0, loop
        addu $2, $2, $5
exit:
        jr $31
        nop
Machine code
18800005
00001025
00451021
0044182a
5460fffe
00451021
03e00008
00000000

---
Circuits: from Verilog to transistors (simplified)
Circuits: from Verilog to transistors (simplified)
module counter
(
    input clock,
    input reset,
    output logic [1:0] n
);
    always @(posedge clock)
    begin
        if (reset)
        n <= 0;
        else
        n <= n + 1;
    end
endmodule

---
What is an FPGA? A simplified explanation
What is an FPGA? A simplified explanation
A matrix of cells with changeable function
One cell can become AND, another OR, yet another - one bit of memory
An FPGA does not contain a fixed CPU, but can be configured to work as a CPU
A picture from http://jjmk.dk/MMMI/PLDs/FPGA/fpga.htm

---
What is inside an FPGA cell?
What is inside an FPGA cell?
Each cell has multiplexers or muxes
A mux is a device that implements choice: “if ” in hardware
Muxes are connected to bits of memory, loaded from outside the FPGA
This allows forming circuits inside an FPGA by changing the contents of configuration memory
Pictures are from https://breadboardgremlins.wordpress.com/what-is-an-fpga/ and http://www2.engr.arizona.edu/~rlysecky/courses/cs168-04w/lab7/lab7.html

---
Twelve basic ideas of digital hardware design
Twelve basic ideas of digital hardware design
- Gate
- Area
- Delay
- Parallelism
- Module
- Testbench
- Clock
- Reset
- D-Flip-Flop
- Power
- Finite State Machine
- Pipeline
We color-code the topics of Lab 1 in green, the topics of Lab 2 in blue and the topics of Lab 3 in purple.

---
A hardware design can be partitioned into
A hardware design can be partitioned into
Combinational logic
  - Used to calculate logic and arithmetical functions
- Sequential logic
  - Allows hardware to have memory and repeat actions
- The first lab covers only combinational logic

---
Combinational logic
Combinational logic
- The outputs of the group of components depend only on inputs
- You set inputs and get outputs after some time
- This group is called “a combinational cloud”
- Used to calculate logic and arithmetical functions
module top
(
   input a, b, c, d,
   output e, f
);
   assign e = a & (b | c);
   assign f = ~ (c ^ d);
endmodule

---
Sequential logic
Sequential logic
- The outputs of the partition depend not only on inputs but also on internal state, stored in registers
- Change of the state is synchronized by a clock signal
- Allows hardware to be smart - memorize the intermediate results and iterate

---
Lab 1 exercises
Lab 1 exercises
Simulating a combinational module
  1. Ports, continuous assignments, testbench, delay, waveforms
  2. We will use ModelSim PE Student Edition from Mentor Graphics
2. Synthesizing a combinational module with basic gates
  1. Logic synthesis, constrains, synthesized schematics, FPGA configuration
  2. We will use Intel Quartus Lite Edition and Terasic DE10-Lite FPGA boards
3. Homework: Synthesize a combinational module that uses input from a button and muxes to output either your first name or last name to a multi-digit 7-segment indicator

---
Clone a repository from GitHub
Clone a repository from GitHub
Organization https://github.com/MIPSfpga
Repository digital-design-lab-manual

---
Exercise 1:
Simulating a combinational module

---
The design module - 1
The design module - 1
- lab_01/src/lab1_hdl/lab1.v
- The unit of design is called “module”
- Module has a name and a list of ports
- Each port has a direction
  - input, output or inout
- Each port has a width / vector dimension
  - “[9:0]” means “10 bits from LED [9] through LED [0]”
  - If no dimension, 1-bit port assumed, such as “input ABC”

---
The design module - 2
The design module - 2
- lab_01/src/lab1_hdl/lab1.v
- “wire” declaration creates an intermediate connection between ports, other wires or “reg” variables to be discussed further
- wire can be 1-bit wide, or multiple bit wide, like “wire [4:0] A”
- The assignments to wires are continuous
  - Every time the expression on right hand side changes, it triggers change of the wire on left hand side
- Wires can be optimized away by the synthesis software

---
The design module - 3
The design module - 3
- lab_01/src/lab1_hdl/lab1.v
- The keyword “assign” is used for continuous assignments to an already declared port or a wire
- Note that the assignments do not assume a specific order - they semantically happen whenever the right hand side changes
- The HDL simulator is event-driven, it schedules the assignment evaluations by putting them into a queue of events
- HDL synthesis simply creates a netlist (graph) for an electric circuit

---
The simulation testbench - 1
The simulation testbench - 1
- lab_01/src/lab1_hdl/simulation/testbench.v
- The testbench module (TB) is for simulation only, it is never synthesized
- TB contains a special program that tests the design module
- The design module instantiated inside TB is frequently referred to as DUT, Design under Test
Testbench (TB)
DUT
(Design under Test)

---
The simulation testbench - 2
The simulation testbench - 2
- lab_01/src/lab1_hdl/simulation/testbench.v
- Testbench
  - Instantiates Design under Test
  - Drives stimulus
  - Checks the responses
- Testbench may also call functions in other languages (like C) to make verification environments more sophisticated
Testbench (TB)
DUT
(Design under Test)

---
The simulation testbench - 3
The simulation testbench - 3
lab_01/src/lab1_hdl/simulation/testbench.v
- Module instantiation connects the design module’s ports to the variables declared in the testbench
- Module instantiation looks like a function call, but it is not.
  - The DUT instance is physically put inside the testbench module
  - The connections between TB variables and DUT ports are continuous, just like the left and right sides of “assign”.

---
The simulation testbench - 4
The simulation testbench - 4
- lab_01/src/lab1_hdl/simulation/testbench.v
- Our TB generates stimulus in the simplest way:
  - Assign a value to a variable connected to DUT input port
  - Wait using #delay construct that causes simulator to postpone the execution of the next statement for a number of specified time units

---
The simulation testbench - 5
The simulation testbench - 5
- lab_01/src/lab1_hdl/simulation/testbench.v
- Keyword “initial” means that the next statement is executed at the beginning of the simulation.
- “begin/end” means that the statements inside are executed sequentially.
- The assignments denoted with “=” inside “begin/end” are called “blocking assignments”. They are executed sequentially, not in parallel (“block the execution”).

---
The simulation testbench - 6
The simulation testbench - 6
- lab_01/src/lab1_hdl/simulation/testbench.v
- The constant 2’b10 means “two bit-wide binary number 10”.
- The time unit in #10 and simulation precision can be specified using `timescale directive. We will see this time later on simulation waveforms. If we put this directive at the beginning of the file, #10 means “10 nanoseconds”:

---
The simulation testbench - 7
The simulation testbench - 7
- lab_01/src/lab1_hdl/simulation/testbench.v
- reg declaration means “a variable that can be assigned inside a begin/end block”
- $monitor statement in initial block tells the simulator to print the specified text into the simulation log whenever any of the variables change

---
The simulation testbench - 8
The simulation testbench - 8
- lab_01/src/lab1_hdl/simulation/testbench.v
- $dumpvar statement in initial block tells the simulator to generate the simulation waveforms.
- A waveform is a database of signal changes for debugging the design.
- The waveform can be viewed in a waveform viewer, either standalone (an example: GTKWave), or integrated into a Verilog simulator.

---
Batch file to run the simulation
Batch file to run the simulation
- lab_01/src/lab1_hdl/simulation/01_simulate_with_modelsim.bat
- Creates a directory for temporary files, produced by ModelSim simulator
- Invokes the simulator executable vsim.
- vsim reads a stream of proprietary commands from a script file written in TCL (Tool Command Language).
If you work under Linux, you can write a shell script that does the same.

---
TCL script file for ModelSim
TCL script file for ModelSim
- lab_01/src/lab1_hdl/simulation/modelsim_script.tcl
- TCL (pronounced "tickle" or tee cee el) is a scripting language used since 1990s in many EDA tools (EDA - Electronic Design Automation).
- You don’t need to know it well, just copy somebody else’s scripts for your projects.

---
Now run everything, modify the code and run again
Now run everything, modify the code and run again

---
Exercise 2:
Synthesizing a combinational module with basic gates

---
The main Quartus project file
The main Quartus project file
- lab_01/src/lab1_hdl/synthesis/lab1.qpf
- It is OK for the Quartus project file to be empty.
- Quartus usually stores some dates and versions there for Intel / Altera customer support.
- All the essential synthesis settings are not in .qpf, but in other files, .qsf and .sdc.
QUARTUS_VERSION = "17.0"
DATE = "12:11:55 November 06, 2017"
PROJECT_REVISION = "lab1"

---
TCL script with synthesis settings - 1
TCL script with synthesis settings - 1
- lab_01/src/lab1_hdl/synthesis/lab1.qsf
- For this project you need only the four directives below, and some signal mapping assignments (see the next slide).
- You don’t need to know all the script commands in the .qsf file.
- Just copy somebody’s script and use the bare minimum settings.
set_global_assignment -name DEVICE 10M50DAF484C7G
set_global_assignment -name TOP_LEVEL_ENTITY lab1
set_global_assignment -name VERILOG_FILE ../../lab1.v
set_global_assignment -name PROJECT_OUTPUT_DIRECTORY .

---
TCL script with synthesis settings - 2
TCL script with synthesis settings - 2
- lab_01/src/lab1_hdl/synthesis/lab1.qsf
- You need to map the port names in your design to the physical pins of the FPGA.
- The synthesis tool know the location of PIN_B8 for chip 10M50DAF484C7G, but it has no idea that the board connects it to a button and you call it KEY[0].
set_location_assignment PIN_B8 -to KEY[0]
set_location_assignment PIN_A7 -to KEY[1]
set_location_assignment PIN_A8 -to LED[0]
set_location_assignment PIN_A9 -to LED[1]
. . . . . . . . . .

---
TCL script with synthesis settings - 3
TCL script with synthesis settings - 3
- lab_01/src/lab1_hdl/synthesis/lab1.qsf
- Your .qsf file has to specify a so-called I/O standard for each signal connected to an FPGA pin.
- You don’t need to know the meaning of the I/O standard property in this course.
- You can use wildcards for signal names when setting IO_STANDARD.
set_instance_assignment -name IO_STANDARD \
    "3.3 V Schmitt Trigger" -to KEY*
set_instance_assignment -name IO_STANDARD "3.3-V LVTTL" -to LED*
. . . . . . . . . .

---
Before synthesis create a copy of project files
Before synthesis create a copy of project files
- lab_01/src/lab1_hdl/synthesis/make_project.bat
- Intel / Altera Quartus Lite Edition creates a lot of temporary files
- It is convenient to run synthesis in a separate directory
- You have to copy project files into that directory
- To do this, run make_project.bat [Windows] / run make_project.sh

---
Run synthesis in Intel Quartus
- File:Open Project
- Do not confuse with File:Open
- Find project file in your temporary project directory
- Do not open project from the original directory
- Double-click “Compile Design” in Tasks window
Run synthesis in Intel Quartus

---
The task window menu has a viewer of FPGA-independent schematics.
It shows the representation of your design after RTL analysis,
but before mapping RTL to specific cells available in this particular FPGA

---
The task window menu also has a viewer of mapped schematics,
where all your logic is mapped to blocks that directly correspond to cells in the target FPGA.
Compare this schematic to the schematic from the previous slide.

---
Terasic DE10-Lite FPGA board
Terasic DE10-Lite FPGA board
- Inexpensive: $85
- Academic price $55
- Intel FPGA MAX 10 10M50DAF484C7G
- 50K cells, enough for designs with CPU cores like MIPSfpga
- On-board 64MB SDRAM
- Connects directly to PC for configuration

---
Configure FPGA on the board - 1
Configure FPGA on the board - 1
- Find and click on “Program Device” in Tasks window
- Programmer window should appear
- If you see “USB-Blaster” next to “Hardware Setup”, the board is connected and found by software
- In this case just press “Start” button

---
Configure FPGA on the board - 2
Configure FPGA on the board - 2
If you see “No hardware”, press “Hardware Setup”

---
Configure FPGA on the board - 3
Configure FPGA on the board - 3
- “Hardware Setup” window should appear with “USB-Blaster” listed under “Hardware”.
- If nothing is listed, check your USB cable connection.
- If the board is connected but nothing is listed, install USB-Blaster driver or resolve driver conflict.

---
Configure FPGA on the board - 4
Configure FPGA on the board - 4
Double-click on “USB-Blaster”, then press “Close”

---
Configure FPGA on the board - 5
Configure FPGA on the board - 5
Now the hardware setup problem should be resolved
Just press “Start” button and see the “Progress” indicator becoming green.
If “Progress” gets stuck, unplug USB cable, plug it in again and repeat.

---
Add a new combinational element - MUX
Add a new combinational element - MUX
- Multiplexers, or muxes, implement the selection between values in hardware.
- The simplest way to infer mux in hardware is to use ternary ?: operation.
- Modify the design with a mux, and re-run synthesis and FPGA configuration.

---
Add new signals to expand the design with MUXes
Add new signals to expand the design with MUXes
- Two keys are not enough to demonstrate a mux because it is a ternary operation. You need to add news signals, connected to buttons and switches on the board
- Use the on-board 7-segment display to output digits or even letters
- Get the full .qsf file for DE10-Lite board from https://github.com/yuri-panchul/2017-year-end/tree/master/terasic_de10_lite

---
Preview
of the next Lab:
Simulating and Synthesizing the Sequential Logic

---
Computation in combinational logic is not instant
Computation in combinational logic is not instant
- It takes time for an electric signal to propagate.
- Before the results are ready, the outputs may contain random values.
- How to find when the results are ready?
- We can synchronize the computations with a special signal called clock.
The picture is from Digital Design and Computer Architecture, 2nd Edition by David Harris and Sarah Harris. Elsevier, 2012

---
Clocks are useful not only to synchronize outputs
Clocks are useful not only to synchronize outputs
- Circuits synchronized with clocks are called sequential.
- Sequential circuits can also have memory and perform iterative computations.
- We will learn about sequential circuits in Lab 2.

---
Thank You!
Thank You!