## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 7
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 7 :: Topics
Introduction
Performance Analysis
Single-Cycle Processor
Multicycle Processor
Pipelined Processor
Exceptions
Advanced Microarchitecture

## Slide 3
Microarchitecture: how to implement an architecture in hardware
Processor:
  Datapath: functional blocks
  Control: control signals
Introduction

## Slide 4
Multiple implementations for a single architecture:
  Single-cycle: Each instruction executes in a single cycle
  Multicycle: Each instruction is broken into series of shorter steps
  Pipelined: Each instruction broken up into series of steps & multiple instructions execute at once
Microarchitecture

## Slide 5
Program execution time
Execution Time = (#instructions)(cycles/instruction)(seconds/cycle)
Definitions:
  CPI: Cycles/instruction
  clock period: seconds/cycle
  IPC: instructions/cycle = IPC
Challenge is to satisfy constraints of:
  Cost
  Power
  Performance
Processor Performance

## Slide 6
Consider subset of MIPS instructions:
  R-type instructions: and, or, add, sub, slt
  Memory instructions: lw, sw
  Branch instructions: beq
MIPS Processor

## Slide 7
Determines everything about a processor:
  PC
  32 registers
  Memory
Architectural State

## Slide 8
MIPS State Elements

## Slide 9
Datapath
Control
Single-Cycle MIPS Processor

## Slide 10
STEP 1: Fetch instruction
Single-Cycle Datapath: lw fetch

## Slide 11
STEP 2: Read source operands from RF
Single-Cycle Datapath: lw Register Read

## Slide 12
STEP 3: Sign-extend the immediate
Single-Cycle Datapath: lw Immediate

## Slide 13
STEP 4: Compute the memory address
Single-Cycle Datapath: lw address

## Slide 14
STEP 5: Read data from memory and write it back to register file
Single-Cycle Datapath: lw Memory Read

## Slide 15
STEP 6: Determine address of next instruction
Single-Cycle Datapath: lw PC Increment

## Slide 16
Write data in rt to memory
Single-Cycle Datapath: sw

## Slide 17
Read from rs and rt
Write ALUResult to register file
Write to rd (instead of rt)
Single-Cycle Datapath: R-Type

## Slide 18
Determine whether values in rs and rt are equal
Calculate branch target address:
BTA = (sign-extended immediate << 2) + (PC+4)
Single-Cycle Datapath: beq

## Slide 19
Single-Cycle Processor

## Slide 20
Single-Cycle Control

## Slide 21
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
Review: ALU

## Slide 22
Review: ALU

## Slide 23
ALUOp1:0 | Meaning
00 | Add
01 | Subtract
10 | Look at Funct
11 | Not Used
ALUOp1:0 | Funct | ALUControl2:0
00 | X | 010 (Add)
X1 | X | 110 (Subtract)
1X | 100000 (add) | 010 (Add)
1X | 100010 (sub) | 110 (Subtract)
1X | 100100 (and) | 000 (And)
1X | 100101 (or) | 001 (Or)
1X | 101010 (slt) | 111 (SLT)
Control Unit: ALU Decoder

## Slide 24
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 |  |  |  |  |  |  | 
lw | 100011 |  |  |  |  |  |  | 
sw | 101011 |  |  |  |  |  |  | 
beq | 000100 |  |  |  |  |  |  | 
Control Unit Main Decoder

## Slide 25
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 0 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
Control Unit: Main Decoder

## Slide 26
Single-Cycle Datapath: or

## Slide 27
No change to datapath
Extended Functionality: addi

## Slide 28
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 |  |  |  |  |  |  | 
Control Unit: addi

## Slide 29
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 | 1 | 0 | 1 | 0 | 0 | 0 | 00
Control Unit: addi

## Slide 30
Extended Functionality: j

## Slide 31
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 |  |  |  |  |  |  |  | 
Control Unit: Main Decoder

## Slide 32
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 | 0 | X | X | X | 0 | X | XX | 1
Control Unit: Main Decoder

## Slide 33
Program Execution Time
= (#instructions)(cycles/instruction)(seconds/cycle)
= # instructions x CPI x TC
Review: Processor Performance

## Slide 34
TC limited by critical path (lw)
Single-Cycle Performance

## Slide 35
Single-cycle critical path:
Tc = tpcq_PC + tmem + max(tRFread, tsext + tmux) + tALU + tmem + tmux + tRFsetup
Typically, limiting paths are:
  memory, ALU, register file
  Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup
Single-Cycle Performance

## Slide 36
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = ?
Single-Cycle Performance Example

## Slide 37
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup
= [30 + 2(250) + 150 + 25 + 200 + 20] ps
= 925 ps
Single-Cycle Performance Example

## Slide 38
Program with 100 billion instructions:
Execution Time = # instructions x CPI x TC
= (100 × 109)(1)(925 × 10-12 s)
= 92.5 seconds
Single-Cycle Performance Example

## Slide 39
Single-cycle:
  + simple
  cycle time limited by longest instruction (lw)
  2 adders/ALUs & 2 memories
Multicycle:
  + higher clock speed
  + simpler instructions run faster
  + reuse expensive hardware on multiple cycles
  - sequencing overhead paid many times
Same design steps: datapath & control
Multicycle MIPS Processor

## Slide 40
Replace Instruction and Data memories with a single unified memory – more realistic
Multicycle State Elements

## Slide 41
STEP 1: Fetch instruction
Multicycle Datapath: Instruction Fetch

## Slide 42
Multicycle Datapath: lw Register Read
STEP 2a: Read source operands from RF

## Slide 43
Multicycle Datapath: lw Immediate
STEP 2b: Sign-extend the immediate

## Slide 44
Multicycle Datapath: lw Address
STEP 3: Compute the memory address

## Slide 45
Multicycle Datapath: lw Memory Read
STEP 4: Read data from memory

## Slide 46
Multicycle Datapath: lw Write Register
STEP 5: Write data back to register file

## Slide 47
Multicycle Datapath: Increment PC
STEP 6: Increment PC

## Slide 48
Write data in rt to memory
Multicycle Datapath: sw

## Slide 49
Read from rs and rt
Write ALUResult to register file
Write to rd (instead of rt)
Multicycle Datapath: R-Type

## Slide 50
rs == rt?
BTA = (sign-extended immediate << 2) + (PC+4)
Multicycle Datapath: beq

## Slide 51
Multicycle Processor

## Slide 52
Multicycle Control

## Slide 53
Main Controller FSM: Fetch

## Slide 54
Main Controller FSM: Fetch

## Slide 55
Main Controller FSM: Decode

## Slide 56
Main Controller FSM: Address

## Slide 57
Main Controller FSM: Address

## Slide 58
Main Controller FSM: lw

## Slide 59
Main Controller FSM: sw

## Slide 60
Main Controller FSM: R-Type

## Slide 61
Main Controller FSM: beq

## Slide 62
Multicycle Controller FSM

## Slide 63
Extended Functionality: addi

## Slide 64
Main Controller FSM: addi

## Slide 65
Extended Functionality: j

## Slide 66
Main Controller FSM: j

## Slide 67
Main Controller FSM: j

## Slide 68
Instructions take different number of cycles:
  3 cycles: beq, j
  4 cycles: R-Type, sw, addi
  5 cycles: lw
CPI is weighted average
SPECINT2000 benchmark:
  25% loads
  10% stores
  11% branches
  2% jumps
  52% R-type
Average CPI = (0.11 + 0.2)(3) + (0.52 + 0.10)(4) + (0.25)(5) = 4.12
Multicycle Processor Performance

## Slide 69
Multicycle critical path:
Tc = tpcq + tmux + max(tALU + tmux, tmem) + tsetup
Multicycle Processor Performance

## Slide 70
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = ?
Multicycle Performance Example

## Slide 71
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = tpcq_PC + tmux + max(tALU + tmux, tmem) + tsetup
= tpcq_PC + tmux + tmem + tsetup
= [30 + 25 + 250 + 20] ps
= 325 ps
Multicycle Performance Example

## Slide 72
For a program with 100 billion instructions executing on a multicycle MIPS processor
  CPI = 4.12
  Tc = 325 ps
Execution Time =
Chapter 7 :: Topics

## Slide 73
For a program with 100 billion instructions executing on a multicycle MIPS processor
  CPI = 4.12
  Tc = 325 ps
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(4.12)(325 × 10-12)
= 133.9 seconds
This is slower than the single-cycle processor (92.5 seconds). Why?

## Slide 74
Program with 100 billion instructions
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(4.12)(325 × 10-12)
= 133.9 seconds
This is slower than the single-cycle processor (92.5 seconds). Why?
Not all steps same length
Sequencing overhead for each step (tpcq + tsetup= 50 ps)
Multicycle Performance Example

## Slide 75
Review: Single-Cycle Processor

## Slide 76
Review: Multicycle Processor

## Slide 77
Temporal parallelism
Divide single-cycle processor into 5 stages:
  Fetch
  Decode
  Execute
  Memory
  Writeback
Add pipeline registers between stages
Pipelined MIPS Processor

## Slide 78
Single-Cycle vs. Pipelined

## Slide 79
Pipelined Processor Abstraction

## Slide 80
Single-Cycle & Pipelined Datapath

## Slide 81
WriteReg must arrive at same time as Result
Corrected Pipelined Datapath

## Slide 82
Same control unit as single-cycle processor
Control delayed to proper pipeline stage
Pipelined Processor Control

## Slide 83
When an instruction depends on result from instruction that hasn’t completed
Types:
  Data hazard: register value not yet written back to register file
  Control hazard: next instruction not decided yet (caused by branches)
Pipeline Hazards

## Slide 84
Data Hazard

## Slide 85
Insert nops in code at compile time
Rearrange code at compile time
Forward data at run time
Stall the processor at run time
Handling Data Hazards

## Slide 86
Insert enough nops for result to be ready
Or move independent useful instructions forward
Compile-Time Hazard Elimination

## Slide 87
Data Forwarding

## Slide 88
Data Forwarding

## Slide 89
Forward to Execute stage from either:
  Memory stage or
  Writeback stage
Forwarding logic for ForwardAE:
if ((rsE != 0) AND (rsE == WriteRegM) AND RegWriteM)
then ForwardAE = 10
else if ((rsE != 0) AND (rsE == WriteRegW) AND RegWriteW)
then ForwardAE = 01
else ForwardAE = 00
Forwarding logic for ForwardBE same, but replace rsE with rtE
Data Forwarding

## Slide 90
Stalling

## Slide 91
Stalling

## Slide 92
Stalling Hardware

## Slide 93
lwstall =
((rsD==rtE) OR (rtD==rtE)) AND MemtoRegE
StallF = StallD = FlushE = lwstall
Stalling Logic

## Slide 94
beq:
  branch not determined until 4th stage of pipeline
  Instructions after branch fetched before branch occurs
  These instructions must be flushed if branch happens
Branch misprediction penalty
  number of instruction flushed when branch is taken
  May be reduced by determining branch earlier
Control Hazards

## Slide 95
Control Hazards: Original Pipeline

## Slide 96
Control Hazards

## Slide 97
Introduced another data hazard in Decode stage
Early Branch Resolution

## Slide 98
Early Branch Resolution

## Slide 99
Handling Data & Control Hazards

## Slide 100
Forwarding logic:
ForwardAD = (rsD !=0) AND (rsD == WriteRegM) AND RegWriteM
ForwardBD = (rtD !=0) AND (rtD == WriteRegM) AND RegWriteM
Stalling logic:
branchstall = BranchD AND RegWriteE AND
(WriteRegE == rsD OR WriteRegE == rtD)
OR
BranchD AND MemtoRegM AND
(WriteRegM == rsD OR WriteRegM == rtD)
StallF = StallD = FlushE = lwstall OR branchstall
Control Forwarding & Stalling Logic

## Slide 101
Guess whether branch will be taken
  Backward branches are usually taken (loops)
  Consider history to improve guess
Good prediction reduces fraction of branches requiring a flush
Branch Prediction

## Slide 102
SPECINT2000 benchmark:
  25% loads
  10% stores
  11% branches
  2% jumps
  52% R-type
Suppose:
  40% of loads used by next instruction
  25% of branches mispredicted
  All jumps flush next instruction
What is the average CPI?
Pipelined Performance Example

## Slide 103
SPECINT2000 benchmark:
  25% loads
  10% stores
  11% branches
  2% jumps
  52% R-type
Suppose:
  40% of loads used by next instruction
  25% of branches mispredicted
  All jumps flush next instruction
What is the average CPI?
  Load/Branch CPI = 1 when no stalling, 2 when stalling
  CPIlw = 1(0.6) + 2(0.4) = 1.4
  CPIbeq = 1(0.75) + 2(0.25) = 1.25
  Average CPI = (0.25)(1.4) + (0.1)(1) + (0.11)(1.25) + (0.02)(2) + (0.52)(1)
  = 1.15
Pipelined Performance Example

## Slide 104
Pipelined processor critical path:
Tc = max {
tpcq + tmem + tsetup
2(tRFread + tmux + teq + tAND + tmux + tsetup )
tpcq + tmux + tmux + tALU + tsetup
tpcq + tmemwrite + tsetup
2(tpcq + tmux + tRFwrite) }
Pipelined Performance

## Slide 105
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Equality comparator | teq | 40
AND gate | tAND | 15
Memory write | Tmemwrite | 220
Register file write | tRFwrite | 100 ps
Tc = 2(tRFread + tmux + teq + tAND + tmux + tsetup )
= 2[150 + 25 + 40 + 15 + 25 + 20] ps = 550 ps
Pipelined Performance Example

## Slide 106
Program with 100 billion instructions
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(1.15)(550 × 10-12)
= 63 seconds
Pipelined Performance Example

## Slide 107
Processor | Execution Time (seconds) | Speedup (single-cycle as baseline)
Single-cycle | 92.5 | 1
Multicycle | 133 | 0.70
Pipelined | 63 | 1.47
Processor Performance Comparison

## Slide 108
Unscheduled function call to exception handler
Caused by:
  Hardware, also called an interrupt, e.g. keyboard
  Software, also called traps, e.g. undefined instruction
When exception occurs, the processor:
  Records cause of exception (Cause register)
  Jumps to exception handler (0x80000180)
  Returns to program (EPC register)
Review: Exceptions

## Slide 109
Example Exception

## Slide 110
Not part of register file
  Cause
    Records cause of exception
    Coprocessor 0 register 13
  EPC (Exception PC)
    Records PC where exception occurred
    Coprocessor 0 register 14
Move from Coprocessor 0
  mfc0 $t0, Cause
  Moves contents of Cause into $t0
Exception Registers

## Slide 111
Exception | Cause
Hardware Interrupt | 0x00000000
System Call | 0x00000020
Breakpoint / Divide by 0 | 0x00000024
Undefined Instruction | 0x00000028
Arithmetic Overflow | 0x00000030
Extend multicycle MIPS processor to handle last two types of exceptions
Exception Causes

## Slide 112
Exception Hardware: EPC & Cause

## Slide 113
Control FSM with Exceptions

## Slide 114
Exception Hardware: mfc0

## Slide 115
Deep Pipelining
Branch Prediction
Superscalar Processors
Out of Order Processors
Register Renaming
SIMD
Multithreading
Multiprocessors
Advanced Microarchitecture

## Slide 116
10-20 stages typical
Number of stages limited by:
  Pipeline hazards
  Sequencing overhead
  Power
  Cost
Deep Pipelining

## Slide 117
Ideal pipelined processor: CPI = 1
Branch misprediction increases CPI
Static branch prediction:
  Check direction of branch (forward or backward)
  If backward, predict taken
  Else, predict not taken
Dynamic branch prediction:
  Keep history of last (several hundred) branches in branch target buffer, record:
    Branch destination
    Whether branch was taken
Branch Prediction

## Slide 118
add $s1, $0, $0 # sum = 0
add $s0, $0, $0 # i = 0
addi $t0, $0, 10 # $t0 = 10
for:
beq $s0, $t0, done # if i == 10, branch
add $s1, $s1, $s0 # sum = sum + i
addi $s0, $s0, 1 # increment i
j for
done:
Branch Prediction Example

## Slide 119
Remembers whether branch was taken the last time and does the same thing
Mispredicts first and last branch of loop
1-Bit Branch Predictor

## Slide 120
Only mispredicts last branch of loop
2-Bit Branch Predictor

## Slide 121
Multiple copies of datapath execute multiple instructions at once
Dependencies make it tricky to issue multiple instructions at once
Superscalar

## Slide 122
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 Ideal IPC: 2
and $t2, $s4, $t0 Actual IPC: 2
or $t3, $s5, $s6
sw $s7, 80($t3)
Superscalar Example

## Slide 123
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 Ideal IPC: 2
and $t2, $s4, $t0 Actual IPC: 6/5 = 1.17
or $t3, $s5, $s6
sw $s7, 80($t3)
Superscalar with Dependencies

## Slide 124
Looks ahead across multiple instructions
Issues as many instructions as possible at once
Issues instructions out of order (as long as no dependencies)
Dependencies:
  RAW (read after write): one instruction writes, later instruction reads a register
  WAR (write after read): one instruction reads, later instruction writes a register
  WAW (write after write): one instruction writes, later instruction writes a register
Out of Order Processor

## Slide 125
Instruction level parallelism (ILP): number of instruction that can be issued simultaneously (average < 3)
Scoreboard: table that keeps track of:
  Instructions waiting to issue
  Available functional units
  Dependencies
Out of Order Processor

## Slide 126
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 Ideal IPC: 2
and $t2, $s4, $t0 Actual IPC: 6/4 = 1.5
or $t3, $s5, $s6
sw $s7, 80($t3)
Out of Order Processor Example

## Slide 127
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 Ideal IPC: 2
and $t2, $s4, $t0 Actual IPC: 6/3 = 2
or $t3, $s5, $s6
sw $s7, 80($t3)
Register Renaming

## Slide 128
Single Instruction Multiple Data (SIMD)
  Single instruction acts on multiple pieces of data at once
  Common application: graphics
  Perform short arithmetic operations (also called packed arithmetic)
For example, add four 8-bit elements
SIMD

## Slide 129
Multithreading
  Wordprocessor: thread for typing, spell checking, printing
Multiprocessors
  Multiple processors (cores) on a single chip
Advanced Architecture Techniques

## Slide 130
Process: program running on a computer
  Multiple processes can run at once: e.g., surfing Web, playing music, writing a paper
Thread: part of a program
  Each process has multiple threads: e.g., a word processor may have threads for typing, spell checking, printing
Threading: Definitions

## Slide 131
One thread runs at once
When one thread stalls (for example, waiting for memory):
  Architectural state of that thread stored
  Architectural state of waiting thread loaded into processor and it runs
  Called context switching
Appears to user like all threads running simultaneously
Threads in Conventional Processor

## Slide 132
Multiple copies of architectural state
Multiple threads active at once:
  When one thread stalls, another runs immediately
  If one thread can’t keep all execution units busy, another thread can use them
Does not increase instruction-level parallelism (ILP) of single thread, but increases throughput
Intel calls this “hyperthreading”
Multithreading

## Slide 133
Multiple processors (cores) with a method of communication between them
Types:
  Homogeneous: multiple cores with shared memory
  Heterogeneous: separate cores for different tasks (for example, DSP and CPU in cell phone)
  Clusters: each core has own memory system
Multiprocessors

## Slide 134
Patterson & Hennessy’s: Computer Architecture: A Quantitative Approach
Conferences:
  www.cs.wisc.edu/~arch/www/
  ISCA (International Symposium on Computer Architecture)
  HPCA (International Symposium on High Performance Computer Architecture)
Other Resources