## Slide 1: Extra slides for MIPSfpga training – 2016 USA
Prerequisites, roadmap and project discussion

## Slide 2: Extra slides for MIPSfpga training
Prerequisites
  What do we expect from the attendees to know
  Pointers to the specific extra slides to understand the missing concepts
  We are interested to accommodate both people with EE and CS backgound
Road map for MIPSfpga
  Additional labs that explore caches, interrupts and memory management
  Labs to investigate the processor’s insides, how pipeline works
  Adding custom instructions using CorExtend / UDI interface (User Defined Instructions)

## Slide 3: Prerequisites
How many of you can program in C?
How many of you understand any assembly language?
  See How to learn MIPS assembly language fast
How many of you know Verilog or VHDL?
  See The concepts of HDL and RTL-to-GDSII design flow
How many of you understand what is FPGA?
  See Intro to FPGAs, the need and the solution
How many of you understand microarchitecture / pipelining?
  Do you know the difference between architecture and microarchitecture?
  If not, see The concepts of microarchitecture and pipelining
Questions to ask before the seminar

## Slide 4: How to learn MIPS assembly language fast
One of prerequisites for using MIPSfpga efficiently

## Slide 5: MARS simulator from University of Missouri
http://courses.missouristate.edu/KenVollmar/MARS/

## Slide 6: HDL and RTL-to-GDSII design flow
One of prerequisites for understanding MIPSfpga

## Slide 7: How SoC and IP blocks are designed
The base is RTL-to-GDSII Design Flow
  The mainstream design methodology during the last 25 years
RTL – Register Transfer Level
  A way to define functionality of a circuit
  Describes how its state changes each clock cycle
  Uses text languages Verilog and VHDL for design entry
GDSII – Graphics Database System II
  SoC designer sends it to the factory to manufacture the chip
  The database format describes the geometrical shapes
  GDSII file is used to create photomasks and finally microchips

## Slide 8: Key steps from RTL to GDSII
Logic Synthesis
  Input: the description of the circuit behavior in Verilog or VHDL
  Output: a graph (called netlist) that consists of logic elements and wires
Placement
  Finds the positions of logic elements on a microchip for maximum efficiency
Routing
  Connecting placed logic elements by wires
Those steps are facilitated by Electronic Design Automation (EDA) software

## Slide 9: An example: a counter described in Verilog
module counter
(
input clock,
input reset,
output logic [1:0] n
);
always @(posedge clock)
begin
if (reset)
n <= 0;
else
n <= n + 1;
end
endmodule

## Slide 10: What the counter circuit does

## Slide 11: The counter circuit after logic synthesis

## Slide 12: How GDSII file looks like
This slide is from course of Charles Dancak cdancak@ucsc.edu in University of California Santa Cruz Silicon Valley Extension

## Slide 13: An example of the final results
A simple implementation of MIPS architecture
Created by students in Harvey Mudd College, California
The source - http://www.staticfreesoft.com/electricGallery.html
After logic synthesis, placement and rounting

## Slide 14: Introduction to FPGAs

## Slide 15: Suppose a student wants to make his own chip
A commercial order for a chip on a foundry like TSMC is too expensive
  > $1M typical initial cost – not for a student’s budget
Using Multi-Project-Wafer (MPW) service through MOSIS or Europractice
  $X0,000 – still too expensive, maybe for very advanced research projects
Simulation using HDL simulation software on a workstation
  Several orders of magnitude slower than a chip
What to do?

## Slide 16: A solution - FPGA
Matrix of interconnected cells with changeable logical function
  The function of a cell is defined by loading bitfile into configuration memory
  Flexibility is achieved by using multiplexers connected to configuration memory bits
Advantages
  Reprogrammable
  Three orders of magnitude faster than software simulation on register transfer level
  Small NRE (non-recurring engineering) cost, student boards start from less than $100
Disadvantages
  Less capacity than ASIC (application-specific integrated cirtcuits)
  Slower than ASIC, allows less clock frequency
  Per unit cost of FPGA is much higher than high-volume ASIC of the same capacity
Field Programmable Gate Array

## Slide 17: Not just for prototyping
In small volumes FPGA can be more cost-efficient than ASIC
The example is from Digital Design and Computer Architecture by David Harris and Sarah Harris, 2012

## Slide 18: An idea about the structure of FPGA
The picture is from http://mazsola.iit.uni-miskolc.hu/cae/docs/pld1.en.html

## Slide 19: How reprogrammability works
Lookup table inside a logic cell uses multiplexers connected to memory bits
The picture is from http://www.eetimes.com/document.asp?doc_id=1274561

## Slide 20: Specifics of Xilinx Artix-7 FPGA used in training

## Slide 21: Specifics of Xilinx Artix-7 FPGA used in training

## Slide 22: Specifics of Xilinx Artix-7 FPGA used in training

## Slide 23: Microarchitecture / pipelining
One of prerequisites for using MIPSfpga efficiently

## Slide 24: A recommended book
See Chapter 7 on microarchitecture
Introduction to all levels of abstraction:
  Digital basics
  Logic design
  Microarchitecture
    CPU blocks, structure of pipeline
    This is how a hardware engineer sees the CPU
  Architecture
    Instruction set
    This is how a software engineer sees the CPU
  Link to OS and applications

## Slide 25: A simple beginner’s CPU from DDCA
A useful prequel to understand pipelining before experimenting with MIPSfpga
The example is from Digital Design and Computer Architecture by David Harris and Sarah Harris, 2012

## Slide 26: An efficient way of teaching
First, students build their own simple CPU to get familiar with concepts of:
  Datapath and controller
  Pipeline and pipeline stages
  Stalls and forwarding
Then, students experiment with a real industrial core, MIPSfpga:
  Add peripherals to MIPSfpga system
  Observe pipeline in action
  Add their own instructions to the CPU using CorExtend interface
  Modify the behavior of caches and memory management unit
  Build multicore systems, with or without cache coherence
    Cache coherence is difficult, requires adding MESI protocol and coherence manager

## Slide 27: MIPSfpga roadmap
Advanced features for Getting Started / Fundamentals

## Slide 28: Planned improvements in MIPSfpga Getting Started
Smaller bootcode - available
  Allows using MIPSfpga with older and cheaper FPGA boards without sacrificing features
    Digilent Basys3, Terasic / Altera DE0, DE0-Nano, DE0-CV, DE1
Loading software programs without BusBlaster and OpenOCD - available
  For Xilinx, a new solution uses embedded UART in Digilent Nexys4 DDR and Basys3
  For Altera, a new solution uses cheap FTDI USB-to-UART connector
VHDL version for top-level modules
Scripts for using MIPSfpga package on Linux
Better documentation that describes the structure of core design
For experimental version see https://github.com/MIPSfpga/mipsfpga-plus
Some of them are already available as experimental MIPSfpga+ version

## Slide 29: Planned improvements in MIPSfpga Fundamentals
More peripherals – include Light sensor – available
Observe work of caches in real time - available
  Cache miss signal is connected to LED
  The core is running on very low frequency (a few cycles per second)
Interrupts
Adding CorExtend / User Defined Instructions
Observing pipeline bypass with different assembly programs
Changing cache replacement policies
Some of them are already available as experimental MIPSfpga+ version

## Slide 30: An example used to demo caches in action
A new version of MIPSfpga has switchable in run-time clock that can run either on 25 MHz or 12.5 Hz
First, the program is run on 25 MHz, than a user switches clock to 12.5 Hz and observes caches misses by watching blinking LED
The example shows different cache behavior when we fill the array by rows-first versus column-first
For experimental version see https://github.com/MIPSfpga/mipsfpga-plus

## Slide 31: Observing pipeline bypasses
This lab also utilized switchable clock

## Slide 32: Adding custom instructions using CorExtend
Another name for CorExtend is UDI, User Defined Instructions, where “user” is “SoC designer”
New instructions are implemented in a separate module with well-defined interface accessible even for beginning students
UDI instructions
  Have access to general-purpose registers
  Do not stall pipeline unless required
  Can have internal state
The protocol include a mechanism for exceptions
See http://zatslogic.blogspot.com/2016/01/using-mips-microaptiv-up-processor.html

## Slide 33: Thank you!